## Slide 1: The Data Link Layer
Chapter 3

## Slide 2: 3.1 Data Link Layer Design Issues
Services Provided to the Network Layer
Framing(成帧)
Error Control(错误控制)
Flow Control(流量控制)
Object : reliable, efficient communication between two adjacent machines.

## Slide 3: Functions of the Data Link Layer
Provide service interface to the network layer
Dealing with transmission errors
Regulating data flow
  Slow receivers not swamped by fast senders

## Slide 4: Functions of the Data Link Layer (2)
Relationship between packets and frames.

## Slide 5: Services Provided to Network Layer
(a) Virtual communication.
(b) Actual communication.

## Slide 6: Services Provided to Network Layer(2)
Various services
  Unacknowledged connectionless service, appropriate for
    Error rate is very low
    Real-time traffic, late data are worse than bad
    Most LANs .
  Acknowledged connectionless service.
    Unreliable channels, such as wireless systems
  Acknowledged connection-oriented service.
    WAN , Point to point
    Establish connection, transmit frames, release connection
    Each frame sent is indeed received exactly once, all frames are received in the right order.

## Slide 7: Services Provided to Network Layer (3)
Placement of the data link protocol.

## Slide 8: Framing
A character stream. (a) Without errors. (b) With one error.
1.Character count (字符计数法)

## Slide 9: Framing (2)
(a) A frame delimited by flag bytes.
(b) Four examples of byte sequences before and after stuffing.
2.Flag bytes with byte stuffing(字符填充法 )

## Slide 10: Framing (3)
Bit stuffing
(a) The original data.
(b) The data as they appear on the line.
(c) The data as they are stored in receiver’s memory after destuffing.
3.Starting and ending flags, with bit stuffing(位填充法)

## Slide 11: Framing (4)
4.Physical layer coding violations(物理层违例编码法)
Manchester encoding
  0: first low and then high;
  1: first high and then low
  First low and then low or first high and then high is violative code.

## Slide 12: Error Control
All frames are eventually delivered to the destination and in the proper order
Error detect
Feedback, positive or negative acknowledgement
T
Sequence number
  Retransmission and reorder

## Slide 13: Flow Control
Sender wants to transmit frames faster than the receiver can accept them.
Feedback-based flow control, permission
Rate-based flow control

## Slide 14: 3.2 Error Detection and Correction
Error-Correcting Codes
  Hamming codes
  Binary convolutional codes
  Reed-Solomon and Low-Density Parity Check codes
  Mathematically complex, widely used in real systems
Error-Detecting Codes
  Parity
  Checksums
  Cyclic redundancy codes

## Slide 15: Hamming distance
Hamming distance is the minimum bit flips to turn one
valid codeword into any other valid one.
Example with 4 codewords of 10:
0000000000, 0000011111, 1111100000, and 1111111111
Hamming distance is 5
Bounds for a code with distance:
2d+1 – can correct d errors(e.g., 2 errors above)
d+1 – can detect d errors(e.g., 4 errors above)

## Slide 16: Error Correction -Hamming codes(1)
Hamming code gives a simple way to add check bits and correct up to a single bit error.
Hamming code include m message bits and r check bits:
(m+r+1)≤2r

## Slide 17: Hamming codes(2)
Use of a Hamming code to correct burst errors.

## Slide 18: Hamming codes(3)
Example
  “H”=1001000
  P1=M1⊕M2 ⊕ M4 ⊕ M5 ⊕ M7=1 ⊕ 0 ⊕ 1 ⊕ 0 ⊕ 0=0
  P2=M1 ⊕ M3 ⊕ M4 ⊕ M6 ⊕ M7=1 ⊕ 0 ⊕ 1 ⊕ 0 ⊕ 0=0
  P3=M2 ⊕ M3 ⊕ M4 ⊕ M8=0 ⊕ 0 ⊕ 1 ⊕0 =1
  P4=M5 ⊕ M6 ⊕ M7 ⊕ M8=0 ⊕ 0 ⊕ 0 ⊕ 0=0
  Codeword=00110010000

## Slide 19: Error-Correcting Codes(4)
海明码是由R. Hamming在1950年首次提出的，它也是一种可以纠正一位差错的编码。
海明码能发现多位错误,但只能纠正一位错，若用在纠正传输中出现突发性差错时可以采用下述方法:将连续P个码字排成一个矩阵，每行一个码字。如果发生突发长度≤P的突发错误，那么在P个码字中最多每个码字有一位有差错，正好由海明码能纠正。

## Slide 20: Error Detection – Parity (1)
Parity bit is added as the modulo 2 sum of data bits
  Equivalent to XOR; this is even parity
  Ex: 1110000  11100001
  Detection checks if the sum is wrong (an error)
Simple way to detect an odd number of errors
  Ex: 1 error, 11100101; detected, sum is wrong
  Ex: 3 errors, 11011001; detected sum is wrong
  Ex: 2 errors, 11101101; not detected, sum is right!
  Error can also be in the parity bit itself
  Random errors are detected with probability ½

## Slide 21: Error Detection – Parity (2)
Interleaving of N parity bits detects burst errors up to N
  Each parity sum is made over non-adjacent bits
  An even burst of up to N errors will not cause it to fail

## Slide 22: Error Detection – Checksums（1）
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words
  Ex: Internet 16-bit 1s complement checksum
Properties:
  Improved error detection over parity bits
  Detects bursts up to N errors
  Detects random errors with probability 1-2N
  Vulnerable to systematic errors, e.g., added zeros

## Slide 23
发送端
接收端
16 位
字 1
16 位
字 2
置为全 0
检验和
16 位
字 n
16 位
反码算术/1的补码算法
运算求和
…
…
取反码
数
据
报
首
部
IP 数据报
16 位
检验和
16 位
字 1
16 位
字 2
16 位
检验和
16 位
字 n
16 位
反码算术
运算求和
16 位
结果
…
…
取反码
数据部分
若结果为 0, 则保留；
否则，丢弃该数据报
数据部分
不参与检验和的计算
Checksum Calculation（2）

## Slide 24: Checksum（Example）
0x D190
4
5
0
30
1
0
0
10
17
100.
102.
0
11010001 10010000
0100
00000000 00011110
00000000 00000001
000
00001010
00000000 00000000
01100100
00001110
01100110
00000111
0101
00000000
00000 00000000
00010001
12.
00001100
14.
00000101
5
00100100
00001001
36.
7.
9
+
1 00101110 01101110
取
反
Checksum：0x D190
IP Header
+
1
00101110 01101111

## Slide 25: Error Detection – CRCs (1)
Adds bits so that transmitted frame viewed as a polynomial is evenly divisible by a generator polynomial
Start by adding 0s to frame and try dividing
Offset by any reminder to make it evenly divisible

## Slide 26: Error-Detecting Codes(2)
Sender and receiver must agree upon a generator polynomial, G(x).
Both the high- and low-order bits of the generator must be 1.
The frame with m bits, corresponding to the polynomial M(x), must be longer than the generator polynomial.
To append a checksum to the end of the frame
When the receiver gets the checksummed frame, it tries dividing it by G(x).
If there is a remainder, there has been a transmission error.

## Slide 27: Error-Detecting Codes(3)
The algorithm for computing the checksum is as follows:
  Let r be the degree of G(x). Append r zero bits to the low-order end of the frame so it now contains m + r bits and corresponds to the polynomial xrM(x).
  Divide the bit string corresponding to G(x) into the bit string corresponding to xrM(x), using modulo 2 division.
  Subtract the remainder (which is always r or fewer bits) from the bit string corresponding to xrM(x) using modulo 2 subtraction.
  The result is the checksummed frame to be transmitted. Call its polynomial T(x).

## Slide 28: Error-Detecting Codes(4)
The power
  Catch all errors consisting of an odd number of inverted bits
  A polynomial code with r check bits will detect all burst errors of length <= r.
A simple shift register circuit can be constructed to compute and verify the checksums in hardware

## Slide 29: Error Detection – CRCs (5)
Based on standard polynomials:
  Ex: Ethernet 32-bit CRC is defined by:
  Computed with simple shift/XOR circuits
Stronger detection than checksums:
  E.g., can detect all double bit errors
  Not vulnerable to systematic errors

## Slide 30: 3.3 Elementary Data Link Protocols
A Utopian Simplex Protocol（理想化单工协议）
A Simplex Stop-and-Wait Protocol for an Error-Free Channel（无噪声信道单工停-等协议）
A Simplex Stop-and-Wait Protocol for a Noisy Channel （有噪声信道单工停-等协议）

## Slide 31
Implementation of the physical, data link, and network layers

## Slide 32: Protocol Definitions
Continued 
Some definitions needed in the protocols to follow. These are located in the file protocol.h.

## Slide 33: Protocol Definitions (ctd.)
Some definitions needed in the protocols to follow. These are located in the file protocol.h.

## Slide 34: Protocol Definitions (ctd.)
Link layer protocol implementations use library functions

## Slide 35: Utopian Simplex Protocol
Assume
  Physical layer, data link layer, and network layer are independent processes
  One direction transmission
  Have a reliable Physical layer service.
  Machine A have an infinite supply of data ready to send
  Machine B always ready to receive
  machines do not crash

## Slide 36: Utopian Simplex Protocol

## Slide 37: Simplex Stop-and-Wait Protocol （Error-Free Channel）
Receiver sends Acknowledgement for flow control
Only one frame out at a time – called stop-and-wait

## Slide 38: Simplex Stop-and-Wait Protocol

## Slide 39: A Simplex Stop-and-Wait Protocol (Noisy Channel)
Unreliable Physical line
Solution（ARQ (Automatic Repeat reQuest)
adds error control）
  Sender sends frame with CRC
  Receiver verifies CRC value and sends ACK or NAK
  Sender sends a new frame when receives an ACK, sends old frame when receives an NAK or timeout.
When ACK lost
  Produce a duplicate frame
  A 1-bit sequence number to distinguish new or old frame

## Slide 40: A Simplex Protocol for a Noisy Channel
A positive acknowledgement with retransmission protocol.
Continued 
Send frame (or retransmission)
Set timer for retransmission
Wait for ack or timeout
If a good ack then set up for the next frame to send (else the old frame will be retransmitted)

## Slide 41: A Simplex Protocol for a Noisy Channel (ctd.)
A positive acknowledgement with retransmission protocol.
Wait for a frame
If it’s new then take it and advance expected frame
Ack current frame

## Slide 42: 停等（stop-and-wait）协议的流程图

## Slide 43: 停—等协议的信道利用率
B is channel capacity (bits/sec)
L is frame size (bits)
R is round-trip propagation time (sec)

## Slide 44: 3.4 Sliding Window Protocols（滑动窗口协议）
Object: more efficient
A One-Bit Sliding Window Protocol
A Protocol Using Go Back N
A Protocol Using Selective Repeat

## Slide 45: Some concepts
Transmit data in two direction
Piggybacking （捎带）
Sliding window
  Sequence number
  Size
  Upper edge and Lower edge
Sending Window
  The frame was sent but no ACK received
  buffer
Receiving Window
  Acceptable Frame

## Slide 46: Sliding Window Protocols (2)
A sliding window of size 1, with a 3-bit sequence number.
(a) Initially.
(b) After the first frame has been sent.
(c) After the first frame has been received.
(d) After the first acknowledgement has been received.
Sender
Receiver

## Slide 47: Sliding Window Protocols(3)
发送4号帧
发送5号帧
接收确认3号帧
接收确认4号帧
接收确认5号帧

## Slide 48: A One-Bit Sliding Window Protocol
Continued 
Prepare first frame
Launch it, and set timer

## Slide 49: A One-Bit Sliding Window Protocol (ctd.)
If a frame with new data then deliver it
Wait for frame or timeout
(Otherwise it was a timeout)
If an ack for last send then prepare for next data frame
Send next data frame or retransmit old one; ack the last data we received

## Slide 50: A One-Bit Sliding Window Protocol (2)
Two scenarios for protocol 4. (a) Normal case. (b) Abnormal case.
Time
Notation is (seq, ack, frame number). Asterisk indicates frame accepted by network layer .
（a）
（b）

## Slide 51: A One-Bit Sliding Window Protocol (3)
B is channel capacity (bits/sec)
L is frame size (bits)
R is round-trip propagation time (sec)
The time needed to transmit a frame
L/B + R/2 + R/2
Line utilization = L / (L + B*R)
Pipelining（流水线）

## Slide 52
讨论：
在协议4中
（1）当发送方在第48页倒数第2行语句中发送的一个数据帧丢失了，接收方执行何种动作？
（2）当发送方在第48页倒数第2行语句中发送的一个数据帧丢失了，发送方执行何种动作？
（3）当接收方正确收到发送方在第48页倒数第2行语句中发送的一个数据帧，并发送了该数据帧的确认，但该确认帧丢失了，发送方执行何种动作？

## Slide 53: Sliding Window Protocol Using Go Back N（1）
Receiver’s window size is 1
Receiver only accept frame in order
Piggyback
Ack for frame n means n - 1, n - 2, and so on are also acknowledged.
Sending window < MAX_SEQ+1
  No more than MAX_SEQ unacknowledged frames outstanding at any time
Bandwidth efficiency is lower
Buffer space is smaller

## Slide 54: Go-Back-N (2)
Receiver only accepts/acks frames that arrive in order:
  Discards frames that follow a missing/error frame
  Sender times out and resends all outstanding frames

## Slide 55: Go Back N（3）
Continued 

## Slide 56: Go Back N（4）
Continued 

## Slide 57: Go Back N（5）
Continued 

## Slide 58: Go Back N（6）

## Slide 59: Go Back N (7)
Simulation of multiple timers in software.

## Slide 60: A Sliding Window Protocol Using Selective Repeat（1）
Sending and receiving window is (MAX_SEQ+1)/2 （?）
Piggyback or independent to send ACK
Send NAK immediately when a error may happened
Bandwidth efficiency is higher
Buffer space is larger

## Slide 61: Selective Repeat（2）
Receiver accepts frames anywhere in receive window
  Cumulative ack indicates highest in-order frame
  NAK (negative ack) causes sender retransmission of a missing frame before a timeout resends window

## Slide 62: A Sliding Window Protocol Using Selective Repeat（3）
Sending and receiving window is (MAX_SEQ+1)/2
  S sends 0,1,2,3,4,5,6
  R accepted and sends ACK0,1,2,3,4,5,6,but lost
  S resend 0
  R sends ACK6 (new 0 received, but no 7)
  S sends 7 (0 to 6 received, so 7)
  R accepts 7 and 0(the old one as new one)
  S sends new 0, rejected by R

## Slide 63
A Sliding Window Protocol Using Selective Repeat (4)
(a) Initial situation with a window size seven.
(b) After seven frames sent and received, but not acknowledged.
(c) Initial situation with a window size of four.
(d) After four frames sent and received, but not acknowledged.
Originals
Originals
Retransmits
Retransmits
New receive window overlaps old – retransmits ambiguous
New and old receive window don’t overlap – no ambiguity
(a)
(b)
(c)
(d)

## Slide 64: A Sliding Window Protocol Using Selective Repeat（5）
Some parameters
  Ack_Received
  Ack_Expected
  Next_Fram_To_Send
  Frame_Expected
  Too_far

## Slide 65: Selective Repeat（6）
Continued 

## Slide 66: Selective Repeat (7)
Continued 

## Slide 67: Selective Repeat (8)
Continued 

## Slide 68: Selective Repeat (9)

## Slide 69
例:长度为2000位的数据帧，在数据传输速率为1 M bps、最大长度为1 km的物理线路上传输。假设线路的单向传输延迟时间为199 ms，试计算下列协议中的物理通信线路可达到的最大利用率？（数据帧的序列号为4位，确认帧的发送时间忽略不计）
  (1)停—等协议
  (2)回退-n帧的滑动窗口协议
(3)选择性重传的滑动窗口协议

## Slide 70: 3.5 Example Data Link Protocols
  Packet over SONET »
  PPP (Point-to-Point Protocol) »
  ADSL (Asymmetric Digital Subscriber Loop) »

## Slide 71: Packet over SONET
Packet over SONET is the method used to carry IP packets over SONET optical fiber links
  Uses PPP (Point-to-Point Protocol) for framing
Protocol stacks
PPP frames may be split over SONET payloads

## Slide 72: PPP (1)
PPP (Point-to-Point Protocol) is a general method for delivering packets across links
  Framing uses a flag (0x7E) and byte stuffing
  “Unnumbered mode” (connectionless unacknow-ledged service) is used to carry IP packets
  Errors are detected with a checksum
IP packet
0x21 for IPv4
标记域:01111110,字符填充;
地址域:总是被设置为11111111,表示所有站点都应该接受该帧。
控制域:缺省值为00000011,表示无序号帧,不提供使用序号和确认的可靠传输。
协议域:指示净负荷中是何种分组,缺省大小为2个字节。
净负荷域:变长,缺省为1500字节
校验和域:2或4个字节

## Slide 73: PPP协议（2）
PPP是点对点协议(Point-to-Point Protocol)的简称，它是一个工作于数据链路层的广域网协议。PPP由IETF (Internet Engineering Task Force)开发，目前已被广泛使用并成为国际标准。无论是同步电路还是异步电路，PPP协议都能够建立路由器之间或者主机到网络之间的连接。
PPP是面向字符的协议，采用字符填充的成帧技术。

## Slide 74: PPP (3)
A link control protocol brings the PPP link up/down
State machine for link control

## Slide 75: PPP – Point to Point Protocol (4)
The LCP frame types.

## Slide 76: PPP会话建立的过程（5）
PPP提供了建立、配置、维护和终止点到点连接的方法。PPP经过以下4个阶段在一个点到点的链路上建立通信连接。
链路的建立和配置协调：通信的发起方发送LCP帧来配置和检测数据链路。LCP帧有链路建立帧、链路终止帧和链路维护帧三种。
链路质量检测：在链路建立、协调之后。这一阶段是可选的。主要用于对链路质量进行测试，以确定其能否为上层所选定的网络协议提供足够的支持，另外若连接的双方已经要求采用安全认证，则在该阶段还要按所选定的认证方式进行相应的身份认证。
网络层协议配置协调：通信的发起方发送NCP帧以选择并配置网络层协议。
关闭链路：通信链路将一直保持到LCP或NCP帧关闭链路或者是发生一些外部事件（如空闲时间超长或用户干预）。

## Slide 77: PPP Architecture（6）
链路控制协议LCP (Link Control Protocol)用于数据链路连接的建立、配置与测试。
NCP (Network Control Protocol)是一组用来建立和配置不同的网络层协议。
第三层 协议
认证和其他选项
链接控制协议
同步或异步物理介质
物理层
数据链路层
网络层
IP
IPX
PPP
PPP协议结构
IPCP IPXCP 其他协议
网络控制协议

## Slide 78: ADSL (1)
Widely used for broadband Internet over local loops
  ADSL runs from modem (customer) to DSLAM (ISP)
  IP packets are sent over PPP and AAL5/ATM (over)

## Slide 79: ADSL (2)
PPP data is sent in AAL5 frames over ATM cells:
  ATM is a link layer that uses short, fixed-size cells (53 bytes); each cell has a virtual circuit identifier
  AAL5 is a format to send packets over ATM
  PPP frame is converted to a AAL5 frame (PPPoA)
AAL5 frame is divided into 48 byte pieces, each of which goes into one ATM cell with 5 header bytes
Notes: Re ATM: ATM was a major technology in the 1990s that was hyped to win in the convergence of the Internet and telecommunications, but IP won instead. The short, fixed-size cells give flexibility (can mix voice and data without having the voice wait for a whole data packet). ATM is now used in niches such as ADSL and WAN links.

## Slide 80: 作业
3.2, 3.5, 3.7, 3.13, 3.14, 3.18, 3.20, 3.22, 3.23, 3.29